Highlighted blocks:

Added:
Adder: An adder for JSR's imm11 and PC. Sends output to a mux going to PC register.
Shifter: Calculates all three shifts for SHF using logic from bit4, bit5, imm4, and sr1_out
On bit4 low, it shifts sr1_out left by imm4 bits, else on bit 5 low it does a logical shift	right on sr1_out by imm4 bits, else it does an arithmetic shift right on sr1_out by imm4	bits
Masker: Used for calculating data on LDB. Using bit0 as a logical enable and mem_wdata as	the input data, it either shifts the input right by 8 bits when logic is high and masks the	MSB when logic is low.
Maskit: A shifter for calculating data during STB, using a control signal for enabling. On logic	low, passes data through. When logic high, it moves the MSB to LSB in MDR by right-	shifting 8 bits.
Modified:
IR: Consolidated adj9 and adj6 modules into Irs outputs. Added outputs for imm5, non-	adjusted offset6, imm4, imm11, and trap_vect8. Added logic signals going out to	control: bit5, bit0, and bit11. Also added output bits for local control: bit4 and bit5l.	Added input from control for JSR: jssr_en.